## Slide 1: Warm-up
How many different kinds of programming loops are there, and what are they?
Why can using variables to name pins be helpful?
What are the 4 pieces of every programming loop?

## Slide 2: Warm-up
How many different kinds of programming loops are there, and what are they?
    2 – for loop and a while loop
Why can using variables to name pins be helpful?
    Variable names can help you keep track of what is connected to each pin, especially when you have 5 different things (LEDs, buzzers, switches) plugged in
What are the 4 pieces of every programming loop?
Initiation, Condition, Update, Statements

## Slide 3: Pink Slips
If you received a pink slip you have a failing grade for this progress report period.
You need to return the slip to me on Monday of next week with a parent signature. THIS IS FOR A GRADE
If you did not receive a pink slip your grade for this assignment is automatically 100

## Slide 4: Today…
Pulse Width Modulation (PWM)
Duty Cycles
Project #3

## Slide 5: What is PWM?
Optical illusion
Idea that you can pulse something off and on really fast (too fast for your brain to notice), to make it look like it’s slowly dimming or brightening
  LEDs (Christmas lights)
  Motors
  Buzzers
  Speakers

## Slide 6
https://www.youtube.com/watch?v=YmPziPfaByw

## Slide 7: High Frequency
Key  Turn on and off REALLY FAST
500 cycles each second
Brain can only register flickering at about 50 cycles per second

## Slide 8: Duty Cycles
The dimming illusion comes from how often the LED stays on versus how much time it stays off
  Duty Cycle
Represented as a percentage
  100% duty cycle  LED stays on 100% of the time
  50% duty cycle  LED stays on half of the time
    Equal time on, equal time off
  25% duty cycle  LED stays on ¼ of the time
    Stays off three times as much as it stays on

## Slide 10: Arduino PWM Pins
Not all digital pins are capable of PWM
  Only the ones marked with a tilde (~)
  3, 5, 6, 9, 10, 11
analogWrite(x, y)
  x  pin you want to create PWM with
  y  a value for how much voltage should be applied to the pin
    Range from 0 to 255
    00V
    255 5V (full power)

## Slide 11
int d = 5; //cycle lasts 5 milliseconds
int led=3;
void setup( ) {
pinMode(led, OUTPUT);
}
void loop( ) {
for (int a=0; a<256; a++) { //brighten
analogWrite(led,a);
delay(d);
}
for (int b=255; b>=0; b--) { //dim
analogWrite(led,b);
delay(d);
}
delay(200); //wait 200ms between cycles
}

## Slide 12: Project #3
Put 1 LED onto PWM, then
Put all 5 LEDs onto PWM at the same time, then
Put all 5 LEDs onto PWM sequentially.
Create your own dimming pattern