## Slide 1: Warm-up
What is the circuit diagram for an LED?
How can you identify the LED cathode?

## Slide 2: Announcements
I have posted the two previous presentations on the class website.
Grading
Assembly

## Slide 3: Today…
Assigning pin numbers to variable names
Use loops to repeat actions

## Slide 4: Variables
Storage locations for data
Need variable name
  No spaces or special characters ($,#,@,*,&,!, etc)
  Can’t start with numbers
Need data type
  int, float, long  numbers
  char  single letters
  string  words (spaces and special characters allowed)
  bool  boolean (TRUE or FALSE)

## Slide 5: Example #1
int led=13;
void setup( ) {
pinMode(led,OUTPUT);
}
void loop( ) {
digitalWrite(led,HIGH);
}

## Slide 6: Example #2
int redled=13;
int blueled=12;
void setup( ) {
pinMode(redled,OUTPUT);
pinMode(blueled,OUTPUT);
}
void loop( ) {
digitalWrite(redled,HIGH);
digitalWrite(blueled,HIGH);
}

## Slide 7: Loops
Used to repeat an action
FOR loops
  Iterate for a specified number of times
WHILE loops
  Iterate WHILE some condition remains true

## Slide 8: Pieces of the Loop
Initiation
  Where should the counter begin?
Condition
  What should I be checking the counter against?
  When counter break the condition, the loop stops
  Escape route
Update
  How should the counter change with each loop?
Statements
  What should happen each time the loop executes?

## Slide 9: Loops
FOR Loop
WHILE Loop
for (initiation; condition; update) {
//statements
}
for (i=0; i<10; i++) {
Serial.println(i);
}
initiation;
while (condition) {
//statements;
update;
}
i=0;
while (i<10) {
Serial.println(i);
i++;
}

## Slide 10: Example #3
Write a code that does the following:
  Blinks an LED 5 times, then
  Blinks a different LED 3 times
  Repeat

## Slide 11
int led1=12; int led2=13; int i,j;
void setup( ) {
pinMode(led1, OUTPUT);
pinMode(led2, OUTPUT);
}
void loop( ) {
for (i=0; i<6; i++) {
digitalWrite(led1, HIGH);
delay(1000);
digitalWrite(led1, LOW);
delay(1000);
}
for (j=0; j<4; j++) {
digitalWrite(led2, HIGH);
delay(1000);
digitalWrite(led2, LOW);
delay(1000);
}
}

## Slide 12: Project #2
Modify the code from yesterday so that it does the following:
  Give each LED pin a variable name. Use it in the code.
  Using FOR loops, code for the following pattern:
    LED1 blinks 8 times (1 second on, 1 second off), then
    LED2 blinks 10 times (1 second on, ½ second off), then
    LED3 blinks 5 times (½ second on, ½ second off), then
    LED4 blinks 4 times (1 ½ second on, 2 seconds off), then
    LED5 blinks 7 times (300 ms on, 250 ms off)
If you have time…
  Change the FOR loops to WHILE loops