## Slide 1: Warm-Up
Why is a shift register useful?
What is the net pin gain for our shift registers?

## Slide 2: Warm-Up
Why is a shift register useful?
Output pin expander – more pins!
What is the net pin gain for our shift registers?
Net gain of 5 pins

## Slide 3: Example Code:
int data=6; int latch=8; int clock=10;
void setup( ) {
pinMode(data, OUTPUT);
pinMode(latch, OUTPUT);
pinMode(clock, OUTPUT);
}
void loop( ) {
digitalWrite(latch, LOW); //prepare for shift
  shiftOut(data, clock, MSBFIRST, B10000110);
  digitalWrite(latch, HIGH); //shift the bits
  }

## Slide 4: Can shift decimal numbers, too
Yesterday, we worked with shifting binary numbers (B10000110)
You can shift decimal numbers, too
  EX: 183, instead of B10110111

## Slide 5: Binary Number Display
Because of this, we can use our LED setup to determine what a decimal number is in binary (between 0 and 255)
Shift the register a decimal number, and the LEDs will display that number in binary.
  ON = 1
  OFF = 0

## Slide 6: Binary Number Display
Use a for loop to cycle through the numbers 0-255
Inside the for loop, Shift that number out to the shift register to display on the LEDs and print out the number to the Serial Monitor
Delay 500ms between shifts