## Slide 1: Warm-up
Grab a temperature sensor if you don’t already have one.

## Slide 2: Double Temp Display
Use your TMP36 Temperature Sensor and 7-segment LEDs to create a digital temperature sensor
Set up the circuit for the temperature sensor.
  Remember, the sensor is ANALOG!
Determine the temperature in Fahrenheit
  Read the value from the sensor
  voltage = (sensor*5000) / 1024
  offset = voltage – 500;
  fahr = (offset/10)*1.8 + 32
Print the ten’s place of the temperature to one 7-segment LED, and the one’s place to the other 7-segment LED
  tens = fahr/10;
  ones = fahr % 10;