## Slide 1: Warm-up
How do your codes for the LED temp and Buzzer temp lab differ?

## Slide 2: What is a function?
Kind of like a variable that stores code
Sections of code can be executed, or “called” just by writing the name of the function
Variety of built-in functions
  digitalWrite()
  analogRead()
You can also create your own

## Slide 3: Why are functions useful?
Modular and reusable
Reduces repetition and inefficiency
Makes code easier to read and easier to follow
Optimizes memory usage

## Slide 4: Where are functions placed?
Outside of the setup() and loop() sections
void setup() {
//
}
myFunction() {
//
}
void loop() {
//
}

## Slide 5: Pieces of a Function
Name – The name of your function
Parameters – Any information that is passed to your function to make it work
Return – Any information that is returned from your function to the void loop()
Statements - The code you want executed each time the function is called
int multiply2(int number) {
int answer = number*2;
return answer;
}

## Slide 6: Calling a Function
Functions have to be called in the void loop() section of our code
int multiply2(int number) {
int answer = number*2;
return answer;
}
void loop() {
int answer = multiply2(5);
Serial.println(answer);
}

## Slide 7: The VOID data type
Data type is used when the function doesn’t return any information
Used in functions that only perform a command
Example: Blinking an LED
void blinkLED() {
digitalWrite(13, HIGH);
delay(1000);
digitalWrite(13, LOW);
delay(1000);
}

## Slide 8: VOID functions can still accept parameters
Example: Modified blinkLEd
void blinkLED(int pin) {
digitalWrite(pin, HIGH);
delay(1000);
digitalWrite(pin, LOW);
delay(1000);
}
void loop() {
blinkLED(13);
blinkLED(12);
}

## Slide 9: Multiple Parameters
You can add more than one parameter to your functions
Example: Control number of blinks
void blinkLED(int pin, int number, int del) {
for (int i=0; i<number; i++) {
digitalWrite(pin, HIGH);
delay(del);
digitalWrite(pin, LOW);
delay(del);
}
}

## Slide 10: Complete Example
int led = 12;
void setup() {
pinMode(led, OUTPUT);
}
void blinkLED(int pin, int number, int del) {
for (int i=0; i<number; i++) {
digitalWrite(pin, HIGH);
delay(del);
digitalWrite(pin, LOW);
delay(del);
}
}
void loop() {
blinkLED(led,5,2500);
}

## Slide 11: Functions Lab
Modify your existing code from you previous temp and buzzer labs to include 2 or more functions
Possible functions:
  Converting analogRead() to Fahrenheit
  Blinking an LED
  Buzzing a buzzer
  Converting to Morse Code