## Slide 1: Warm-up
Review your quiz. The red grade is your original earned grade. The blue grade is the curved grade.
Highest grade was 100, lowest grade was 45.
If you are on the lower end of the spectrum please consider coming to tutorials and asking for help.

## Slide 2: Reading in Multi-digit Numbers
Serial.read() - ‘0’ reads in first digit only
We need to read in 3

## Slide 3: For Loops vs While Loops
for(start; condition; increment)
{
Statements
}
While (condition)
{
Statements
}

## Slide 4: Reading in Multi-digit Numbers
while (Serial.available() > 0) //this will ensure that the statements in the while loop repeat while there are still numbers in the Serial Monitor
{
shift digits
Read in from Serial Monitor
}

## Slide 5: Shifting Digits
int answer = 0;
answer = answer * 10; //this will shift whatever digit you’re on one to the left.
int z = Serial.read() –’0’;
answer = answer + z;
EX: If we type in 345, the first time we will read in 3 and this will get shifted to 30. Next time the loop runs we will read in 4 and this will get added to the 30 giving us 34. This will then get shifted to 340. Next we read in 5 and add it to 340 giving us 345. Since there are no more digits to read the loop ends.

## Slide 6: Reading in Multi-digit Numbers
Serial.flush();  Clears Serial Monitor
while (Serial.available() == 0)
{
// do nothing until something comes into the serial buffer
}

## Slide 7: Multi-Digit Binary Display
Wire 8 LED’s to your shift register (sorry)
Write code that will accept multi-digit numbers
Shift that number out to the LED’s to create a Multi-digit Binary Display
(Shifting code will be similar to previous Binary Display Lab)