## Slide 1: Warm-up
Why would you need to use a random number for an Arduino project?

## Slide 2: Random Number Generation
Really useful for making dice or lottery games, or interesting lighting effects with the Arduino
Arduino has a pseudo-random number generator
  Each number is random compared to the rest
  The random numbers will always be the same
[23, 45, 12, 56, 78, 34, 67, 21, 90, 43, 13, 95, 83, 21, …]
Use randomSeed() function to get a truly random number

## Slide 3: randomSeed( )
Says where in the array the random number generator should start choosing numbers
Always added to the void setup( ) function
[23, 45, 12, 56, 78, 34, 67, 21, 90, 43, 13, 95, 83, 21, …]
Without randomSeed( ), we would always start at 23, then go to 45, then 12, … etc
void setup() {
randomSeed(4); //start at position 4  (78)
}

## Slide 4: Using an Empty Analog Pin
Typically, the number chosen for the seed is taken from an empty analog pin
Values at empty analog pins bounce constantly between 0 and 1055 (due to static electricity in the air)
This will begin our random number sequence at a (roughly) different spot each time
void setup() {
randomSeed(analogRead(0));
}

## Slide 5: random()
The random() function can be used to generate a random number between two bounds
Minimum is inclusive
Maximum is exclusive
Example: Generate a random number between 1 and 10
int a = random(1, 11);

## Slide 6: Example
int r = 0;
void setup() {
randomSeed(analogRead(0));
Serial.begin(9600);
}
void loop() {
Serial.print(“Random number between 1 and 1000 is: “);
r = random(1, 1001);
Serial.println(r);
delay(1000);
}

## Slide 7: Random Light Display Lab
Set up 7 LEDs in a row
  Make sure to put them in numerically adjacent pins
  EX: pins 3,4,5,6,7,8,9 OR pins 7,8,9,10,11,12,13
Generate a random number between your pin numbers
  EX: IF your LEDs are in pins 3-9, generate a random number between 3 and 9
Use randomSeed(analogRead(0)) in the setup( )
Blink the randomly chosen LED briefly
Repeat for an interesting and random light display