## Slide 1: Warm-Up
What is a function?
Where are functions written?
What is the void data type?

## Slide 2: Warm-Up
What is a function?
A variable that holds lines of code that can be called and executed on demand
Where are functions written?
Between the setup() and loop() functions
What is the void data type?
Represents “no data”; used in functions that don’t return any values

## Slide 3: Serial Monitor
Arduino program comes equipped with a Serial monitor that allows for raw data input and output, as well as communication between the Arduino and the user
Accessed by clicking the magnifying glass in the corner of the screen when the Arduino is running and plugged into a computer
Consists of the Serial object, and a variety of methods

## Slide 4: Methods Associated with Serial
Serial.begin()  tells the Arduino the frequency at which to transmit data (standard is 9600 baud)
  Serial.begin(9600);
Serial.println()  prints a variable or string to the Serial monitor
  Serial.println(temp);
Serial.read()  reads information inputted into the Serial monitor by the user;
  numBlinks = Serial.read();
Serial.available()  checks to see if a value has been inputted into the serial monitor
  Returns 0 if nothing is available to read

## Slide 5: Accepting User Input
First, check if the user has actually typed anything in
  Serial.available() > 0
If Serial.available > 0, read the value in the monitor and save it in a variable
  int variable = Serial.read()

## Slide 6: Example: Reading an Inputted Value from the Serial Monitor
int incoming = 0;
void setup() {
Serial.begin(9600);
}
void loop() {
if (Serial.available() > 0) {
incoming = Serial.read()- ’0’;
Serial.print(“I received: “);
Serial.println(incoming, DEC);
}
}

## Slide 7: Serial Functions Lab
Write a program that allows the user to decide how many times an LED should blink
The program should use a function to make the LED blink
The function should be passed the user-inputted number as a parameter
BONUS: Set up 2 LEDs, then allow the user to choose which LED to blink