## Slide 1: Warm-Up
What is 9 in binary?
What is 110 as a decimal number?

## Slide 2: Warm-Up
What is 9 in binary?
9 = 8 + 1 = 23 + 20  1001
What is 110 as a decimal number?
110 = 22 + 21 = 4 + 2  6

## Slide 3: Limitation of Arduino Pins
Arduino board has 14 digital pins that we can use as output or input
  Pins 0-13
As you can guess, sometimes 14 pins just isn’t really enough

## Slide 4: Shift Registers
Used to add more outputs
What is it?
  An integrated circuit (IC) with 8 digital output pins that can be controlled by sending a byte of data to the IC

## Slide 6: About the 74HC595 Shift Register
8 digital outputs that operate exactly like the Arduino digital outputs
Takes up 3 digital outputs on the Arduino to control the 8 digital outputs it contains
NET GAIN = 5 DIGITAL OUTPUT PINS

## Slide 7: Controlling Pins with the Shift Register
Send the shift register a single byte of data
  EX: B10000110
Each 1 or 0 turns one of the shift register’s outputs on or off
  Pins are counted right to left, beginning with 0
This example turns pins 7, 2, and 1 on

## Slide 8: 74HC595 Shift Register Pin-Out

## Slide 9: Output Pins

## Slide 10: GROUND Pin

## Slide 11: Power Source (+5V)

## Slide 12: Latch and Clock Pins

## Slide 13: Data Pin

## Slide 15: Code Needed to Shift Bits
shiftOut(dataPin, clockPin, bitOrder, value)
dataPin = Arduino pin that is connected to pin 14 on the shift register
clockPin = Arduino pin that is connected to pin 11 on the shift register
bitOrder = MSBFIRST (7 to 0) or LSBFIRST (0 to 7)
value = the value to shift out (as a decimal number or as a binary byte)

## Slide 16: Example Code:
int data=6; int latch=8; int clock=10;
void setup( ) {
pinMode(data, OUTPUT);
pinMode(latch, OUTPUT);
pinMode(clock, OUTPUT);
}
void loop( ) {
digitalWrite(latch, LOW); //prepare for shift
  shiftOut(data, clock, MSBFIRST, B10000110);
  digitalWrite(latch, HIGH); //shift the bits
  }

## Slide 17: Shifting Registers
Using the shift register,
  Make all 8 LEDs light up, then wait 1 second
  Make the first 4 LEDs light up, wait 1 second
  Make the last 4 LEDs light up, wait 1 second
  Make every other LEDs light up, wait 1 second