## Slide 1: Warm-up
What is the difference between input and output?
What would an if statement be used with (input or output)?
If you are finished with your RGB LED Lab place it back in the LED box at the front of the class.
You will also need to pick up ONE push button and ONE capacitor and ONE 10k Ohm Resistor per team. Put them in your kit.

## Slide 2: Four Year Plan
Sign it

## Slide 3: Warm-up
What is the difference between input and output?
Input senses information given to the circuit, output gives information/voltage
What would an if statement be used with (input or output)?

## Slide 4: Warm-up
What is the difference between input and output?
Input senses information given to the circuit, output gives information/voltage
What would an if statement be used with (input or output)?
Input

## Slide 5: Today…
Inputs and outputs
Switches
Capacitors
Project #4 - Circuit

## Slide 6: Inputs and Outputs
Output  information goes OUT of the Arduino and into the system
  Activating something in the circuit
  LEDs, buzzers, displays
Input  information goes INTO the Arduino from the system
  Gives the Arduino information about the system
  Used to make decisions
  Switches, sensors, microphone, buttons

## Slide 7: Switches
INPUT DEVICE
Two states, OPEN or CLOSED
OPEN switch
  Current cannot flow
  Broken wire
  “OFF” state
CLOSED switch
  Current is able to flow
  “ON” state

## Slide 8: Common Switches
ROCKER
PUSH BUTTON
SLIDE
TOGGLE
KEY

## Slide 9: Push Button
Default position is “open”
  Circuit is “off”
Press down, position is “closed”
  Circuit is “on”

## Slide 10: Using Your Push Button

## Slide 11: Using Your Push Button
SIDE 1
SIDE 2

## Slide 12: Using Your Push Button
SIDE 1
SIDE 2

## Slide 13: Using Your Push Button
SIDE 1
SIDE 2

## Slide 14: Using Your Push Button
SIDE 1
SIDE 2

## Slide 15: Using Your Push Button
SIDE 1
SIDE 2

## Slide 16: Using Your Push Button
SIDE 1
SIDE 2

## Slide 17: Capacitor
Electronic component that holds electrical charge
  Kind of like a battery
Consists of two metal plates that trap electrons between them, discharging them after it becomes “full”
Capacitance  measure of how much charge a capacitor can store before discharging
  Measure in farads (F)
    One farad is HUGE, so most capacitors will come in nF or μF

## Slide 18: Types of Capacitors
Ceramic
  Small amounts of charge
    Charge and discharge quickly
  Not polarized
  High frequency circuits
Electrolytic (Aluminum)
  Can hold large charges
  Polarized (have a pos (+) and neg (-) side)
  Noise filters

## Slide 19: Project #4
Design a circuit with a switch, an LED, and a capacitor
Write a program that will turn on the LED for half a second whenever the button is pressed
Working on this circuit today and tomorrow

## Slide 20: Tomorrow: The Algorithm
Check to see if the button has been pressed.
If the button has been pressed, turn on the LED for half a second, then turn if off.
If the button has not been pressed, do nothing.
Repeat indefinitely.

## Slide 21
Materials:
560-Ohm resistor
LED (any color)
100nF capacitor
10 K-Ohm resistor
Push-button switch
Arduino
USB cable
Jumper wire
Breadboard
DO NOT PLUG IN YOUR ARDUINO UNTIL I’VE CHECKED YOUR CIRCUIT

## Slide 22: Warm-up
How are switches and if conditions related?

## Slide 23: Overview
Conditional Statements
Comparators
Booleans
Project #4 - Programming

## Slide 24: Conditional Statements
Check to see IF something is true or false
Execute different lines of code based on the answer
IF this is true, do this
IF this is not true, do something else
Based on either COMPARISON or BOOLEAN Logic

## Slide 25: Syntax – IF Statements
if (condition)
{
statements;
}
else
{
statements;
}
***Additional conditions can be included with the “else if” statement
if (condition) { }
else if (condition) { }
else { }

## Slide 26: Types of Comparators
Less than (<)
Greater than (>)
Less than or equal to (<=)
Greater than or equal to (>=)
Equal to (==)
Not equal to (!=)
Logic statement returns a TRUE or a FALSE

## Slide 27: Examples
x = 5 y = 4 z = 7
x > y  true
z == y  false
x + z > 11  true
x + y != z + 2  false

## Slide 28: Booleans
Exists in one of two states
  TRUE or FALSE
  HIGH or LOW
  1 or 0
Used often with microcontrollers
If this pin is HIGH, do this
If this pin is LOW, do this

## Slide 29: digitalRead( )
Function used to read a digital input pin as HIGH or LOW
Syntax:
digitalRead(pin#);
Return:
HIGH or LOW

## Slide 30: Example – IF Statements
void setup( ) {
pinMode(3, OUTPUT);
pinMode(4, INPUT);
}
void loop( ) {
if (digitalRead(4) == HIGH) {
digitalWrite(3, HIGH);
} else {
digitalWrite(3, LOW);
}
}

## Slide 31: #define
#define RedLED 13
#define BlueLED 12
Place this above void setup () to declare your variables

## Slide 32
Algorithm:
Check to see if the button has been pressed.
If the button has been pressed, turn on the LED for half a second, then turn if off.
If the button has not been pressed, do nothing.
Repeat indefinitely.

## Slide 33
Algorithm:
Check to see if the button has been pressed.
If the button has been pressed, turn on the LED for half a second, then turn if off.
If the button has not been pressed, do nothing.
Repeat indefinitely.

## Slide 35: Advanced Assignment
Adjust the length of time the light stays on when you press the button (+1 pt)
Adjust the program so that the light stays on as long as the button is held down (+1 pt)
Add an additional LED to your circuit, so that 2 LEDs turn on when you press the button. (+3 pts)