## Slide 1: Warm-Up
DO NOT LOG IN
DO NOT GET YOUR KITS
  We are changing partners

## Slide 2: Announcements
Grading will be different

## Slide 3: Warm-Up
What is wrong with this code?
#define LED1 13
pinMode(LED1, OUTPUT);
if(digitalRead(LED1 == HIGH)
digitalWrite(LED1, LOW);

## Slide 4: Warm-Up
What is wrong with this code?
#define LED1 13
pinMode(LED1, OUTPUT);
if(digitalRead(LED1 == HIGH) (digitalRead only works for inputs)
digitalWrite(LED1, LOW);

## Slide 5: Temperature
Measure using a thermistor, a sensor that changes resistance in response to temperature
  High temp = low resistance
  TMP36 temperature sensor
Analog or digital?
Input or output?

## Slide 7: Analog Input
Temperature is an analog input
Convert the reading from the sensor into an actual temperature value
Conversion:
Voltage = ((sensor*5000)/1024) – 500
Celsius = Voltage / 10
Fahrenheit = Celsius*1.8 + 32

## Slide 8: Project #8
Build a temperature sensing circuit
Use red, green, and blue LEDs to indicate hot, mild, and cold temperatures

## Slide 9: Warm-up
How many different circuits do you need to wire for this project?
How many output and input?

## Slide 10: Warm-up
How many different circuits do you need to wire for this project?
  4
How many output and input?
  3 Output
  1 Input (which does not need to be declared)

## Slide 11: Correction

## Slide 12: Communicating
Serial.begin(9600);
  Sets the speed at 9600 BPS for communication between the Arduino and the computer
  Do this in void setup( )

## Slide 13: Reading Analog Signals
analogRead(Pin#);

## Slide 14: Printing Your Results
Serial.print( );
Serial.println( );

## Slide 15: Programming Algorithm
Read the value from the sensor
Convert the sensor reading to a temperature in Fahrenheit
  Voltage = (sensor*5000)/1024
  Voltage = Voltage – 500;
  Celsius = Voltage / 10
  Fahrenheit = Celsius*1.8 + 32
  Use floats for your calculations
If the temp > 80, turn on a red LED
If 60 < temp < 80, turn on a green LED
If temp < 60, turn on a blue LED